## Slide 1: Notes Code Andreas
vb, 23.04.2024
Book: 2013_Book_StructuralAnalysisWithTheFinit.pdf (saved on my desktop)
Codes: Integration_LayerElement.py; Stresses_mixreinf.py

## Slide 2: Contents
Integration_LayerElement.py
Stresses_mixreinf.py
Required input parameters (acc. To „MAT“, geom)

## Slide 3: Integration_LayerElement.py – OVERVIEW
Function definitions
def dh_kij(e_kij, s_kij, k, i, j, cm_k) return Dmh,Dmbh,Dbh,Dsh
def k_k(Bm_k,Bb_k,Bs_k,Jdet_k,e_k,s_k, k, cm_k) return Ke
Undefined Matrices:
GEOMK
MATK
ELEMENTS
COORD
rotLG
ELS
copln
gauss_points and gauss_order
Undefined functions:
get_et

## Slide 4: Required inputs for defining stiffness matrices K_i
GEOMK Geometrical properties like
  Height of entire element
  Height of layer
  a_k (?)
MATK Material parameters like
  E_c
  nu_c
ELEMENTS ?
COORD Coordinates?
rotLG Rotation matrix?
ELS ?
copln ?
gauss_points and gauss_order can find this on internet
get_et  function to get constitutive matrix

## Slide 5: Integration_LayerElement.py (Function 1)
def dh_kij(e_kij, s_kij, k, i, j, cm_k)
return Dmh,Dmbh,Dbh,Dsh
Matrices Dmh, Dmbh, Dbh, Dsh  definition see book, p. 393 Eq. (7.19)
Dmh, Dmbh: Membrane force stiffness (and mixed stiffness)
Dbh: Bending moment stiffness
Dsh: Transverse shear stiffness
k, i, j: Location at which the matrix is to be evaluated
cm_k = ?
Function requires a definition of two constitutive matrices D_p and D_s (book p. 394, Eq. (7.24b))  get_et function called (not defined…)

## Slide 6: Integration_LayerElement.py (Function 2)
def k_k(Bm_k,Bb_k,Bs_k,Jdet_k,e_k,s_k, k, cm_k) return Ke
Definition of B_m, B_b and B_s see book p.402, Eq. (7.56)
E_k, s_k, k: values for strains and stresses passed to dh_kij function
Calculation of K_i with Eq. (7.57), book p.402
Summation of all K_i to receive entire stiffness matrix

## Slide 7: Stresses_mixreinf.py – OVERVIEW
class stress()
def __init__(self,cm_klij,MAT,GEOM)
def principal(self.ex, self.ey, self.gxy) return self.e1, self.e3, self.th
def t_mat(self.th) return self.Tsigma, self.Tepsilon)
def fcs(self.fcp, self.e1) return self.fc
def sc_kfm(self.fcs, self.ec0, self.ect, self.Ec, self.e) return self.sc3
def sc_sargin(self.fcs, self.Ec, self.ec0, self.e) return self.sc3
def ss_bilin(self.es, f_sy, E_s, E_sh) return self.ss
def ssr_tcm(self.e, srm, rho, d, fsy, fsu, Es, Esh, tb0, tb1, Ec) return self.ssr
def sr0_vc(self.th, self.fct, self.rhox, self.dx, self.dy, self.tb0) return self.srx0, self.sry0, self.sr, self.srx, self.sry
Reinforcing steel

## Slide 8
class stress() [continued]
def sigma_cart_1(self) return self.sx, self.sy, self.txy
def sigma_cart_31(self) return self.v, self.sx, self.sy, self.txy
def sigma_cart_32(self) return self.sx, self.sy, self.txy, self.ssx, self.ssy, self.scx, self.scy
def sigma_cart_33(self) return self.sx, self.sy, self.txy, self.ssx, self.ssy, self.scx, self.scy
def sigma_shear(self.E, self.nu) return self.ET, self.txz, self.tyz
def out(self.e) return self.s
Stresses_mixreinf.py – OVERVIEW
For linear elastic material law; can easily be adjusted to incorporate E_steel instead of E_concrete
Important function to determine the stresses based on strains, calling all other relevant functions

## Slide 9: Fragen an Andreas:
Allgemein:
Hast du ein Beispiel, bei dem du auch Zahlen verwendet hast für die MAT / GEOM – Einträge?
Gibt es einen „main“ code oder so, von dem die Funktionen abgerufen werden?
Ich meinte du hattest auch ein File in dem die FE ausgeführt / gesolved wird… hast du das noch?
Im File „Integration_LayerElement.py“ wird gar nicht auf die Klasse „stresses()“ zugegriffen. Wo ist der Zusammenhang?
Spezifischer:
Im File „Integration_LayerElement.py“:
  Es scheinen alle Matrizen nicht definiert zu sein „GEOMK, MATK, ELEMENTS, COORD, ..“: Habe ich ein File nicht erhalten? Oder wo wird das definiert?
  Die Funktion „get_et“ ist nicht definiert. Wo kann ich diese finden / was sollte sie machen?
Im File „Stresses_mixreinf.py“:
  Was ist «defcplx» (Zeile 4)?  Wird im file nicht verwendet..? / gemäss meiner google-suche ist das kein bekanntes package
Ist cm_k dasselbe wie cm_klij?